## Slide 1: SOFA Framework
Dr. Shifa Sulaiman
Robotica Medica – SOFA
Presented by,
Dr. Shifa Sulaiman
Postdoctoral Researcher
ICAROS
UNINA

## Slide 2: SOFA - Simulation Open Framework Architecture
Arose from research in 2006 in
Need for a collaborative framework for physics simulation
SOFA Project definition:
  “Being the open-source reference for interactive and real- time applications”
Applications like:
  Physics animation for Computer Graphics
  Medical Simulation
All applications that need a common simulation tool for model creation, loading of animate a mesh, etc…
Very useful SOFA guide:
  youtube.com/watch?v=KHTAgD1oG8Y&t=3850s

## Slide 3: SOFA Framework
What really is SOFA? A physics engine!
  It is a framework that implements a mathematical model describing the physics around us
  Providing also all the algorithms that solve the physics at each time step
We are interested in using SOFA for:
  Soft and rigid body dynamics
    Medical Simulation
    Robotics and Control

## Slide 4: SOFA Software Architecture
Stable core:
  written in C++: classes that implement the models, solvers, etc.
  Open-source available on Github: LGPL license (download and use it for free!)
  github.com/sofa-framework/sofa
Development of plugins (free-to-define license)
Multi-platform (Linux, Windows, McOS)
Documentation:
  User online: sofa-framework.org/community/doc
  API: sofa-framework.org/api

## Slide 5: SOFA Application
InfinyTech3D (infinytech3d.com/), ROS, 3D Slicer
  Create hyper-realistic simulations

## Slide 6: SOFA Architecture
C++ classes
Contains all physical models, algorithms, and simulation mechanisms
Structure:
  SofaKernel/: Base C++ classes that implement the API of SOFA
    BaseModules
  modules/: all the solvers and algorithms are here (ex: FEM)
  examples/: examples of scenes and simulations
  applications/plugins/: contains optional features, called plugins, that are disabled by default. But we can activate them if we need them (ex: SofaPython plugin)

## Slide 7: Download & Install SOFA
Two ways:
  Download Binaries sofa-framework.org/download/
  Download the source code:
    Configure with Cmake-GUI
  Follow the tutorial step-by-step:
    sofa-framework.org/community/doc/getting- started/build/linux/
Video tutorial:
  youtube.com/watch?v=5pbT49t9M_k

## Slide 8: SOFA GUI
Build-in Graphical User Interface (GUI): GUI runSofa
Running the SOFA executable: $ ./runSofa

## Slide 9: SOFA Main Principles
Scene Graph (Direct Acyclic Graph):
  The graph describes the simulation in
every aspect
  Composed of nodes in a hierarchy
  root is the main, the others are child nodes (objects in the simulation scene)
  Each node has Components: C++ classes, describing the physics of that object
  Each Component has parameters called,
Data (topology, geometry, etc…)
  It is described using XML or Python

## Slide 10: SOFA Main Principles

## Slide 11: SOFA Main Principles

## Slide 12: SOFA Main Principles

## Slide 13: SOFA – Using Python Intrepreter
# Required import for SOFA within python
import Sofa
def main():
# Call the SOFA function to create the root node
root = Sofa.Core.Node("root")
# Call the createScene function, as runSofa does
createScene(root)
# Once defined, initialization of the scene graph
Sofa.Simulation.init(root)
# Run as many simulation steps (here 10 steps are computed)
for iteration in range(10):
Sofa.Simulation.animate(root, root.dt.value)
# Same createScene function as in the previous case
def createScene(rootNode):
#Doesn't do anything yet
return rootNode
# Function used only if this script is called from a python environment
if __name__ == '__main__':
main()

## Slide 14: SOFA – Using runSofa GUI
def main():
# Call the SOFA function to create the root node
root = Sofa.Core.Node("root")
# Call the createScene function, as runSofa does
createScene(root)
# Once defined, initialization of the scene graph
Sofa.Simulation.init(root)
# Launch the GUI (qt or qglviewer)
Sofa.Gui.GUIManager.Init("myscene", "qglviewer")
Sofa.Gui.GUIManager.createGUI(root, __file__)
Sofa.Gui.GUIManager.SetDimension(1080, 800)
# Initialization of the scene will be done here
Sofa.Gui.GUIManager.MainLoop(root)
Sofa.Gui.GUIManager.closeGUI()

## Slide 15: SOFA – Using runSofa GUI
def createScene(rootNode):
rootNode.addObject("VisualGrid", nbSubdiv=10, size=1000)
confignode = rootNode.addChild("Config")
confignode.addObject('OglSceneFrame', style="Arrows", alignment="TopRight")
# Creating the falling sphere object
sphere = rootNode.addChild("sphere")
sphere.addObject('MechanicalObject', name="mstate", template="Rigid3", translation2=[0., 0., 0.],
rotation2=[0., 0., 0.], showObjectScale=50)
#### Visualization subnode for the sphere
sphereVisu = sphere.addChild("VisualModel")
sphereVisu.loader = sphereVisu.addObject('MeshOBJLoader', name="loader",
filename="mesh/ball.obj")
sphereVisu.addObject('OglModel', name="model", src="@loader", scale3d=[50]*3, color=[0., 1., 0.],
updateNormals=False)
sphereVisu.addObject('RigidMapping’)

## Slide 16: SOFA – Using runSofa GUI
rootNode.gravity=[0.0,-9.81,0.0]
rootNode.dt=0.01
totalMass = 1.0
volume = 1.0
inertiaMatrix=[1., 0., 0., 0., 1., 0., 0., 0., 1.]
# Creating the falling sphere object
sphere = rootNode.addChild("sphere")
sphere.addObject('EulerImplicitSolver', name='odesolver')
sphere.addObject('CGLinearSolver', name='Solver', iterations=25, tolerance=1e-05, threshold=1e-05)
sphere.addObject('MechanicalObject', name="mstate", template="Rigid3", translation2=[0., 0., 0.], rotation2=[0., 0., 0.], showObjectScale=50)
sphere.addObject('UniformMass', name="mass", vertexMass=[totalMass, volume, inertiaMatrix[:]])
sphere.addObject('UncoupledConstraintCorrection')

## Slide 17: SOFA – Using runSofa GUI
# Creating the floor object
floor = rootNode.addChild("floor")
floor.addObject('MechanicalObject', name="mstate", template="Rigid3", translation2=[0.0,-300.0,0.0], rotation2=[0., 0., 0.], showObjectScale=5.0)
floor.addObject('UniformMass', name="mass", vertexMass=[totalMass, volume, inertiaMatrix[:]])
#### Collision subnode for the floor
floorCollis = floor.addChild('collision')
floorCollis.addObject('MeshOBJLoader', name="loader", filename="mesh/floor.obj", triangulate="true", scale=5.0)
floorCollis.addObject('MeshTopology', src="@loader")
floorCollis.addObject('MechanicalObject')
floorCollis.addObject('TriangleCollisionModel', moving=False, simulated=False)
floorCollis.addObject('LineCollisionModel', moving=False, simulated=False)
floorCollis.addObject('PointCollisionModel', moving=False, simulated=False)
floorCollis.addObject('RigidMapping')
#### Visualization subnode for the floor
floorVisu = floor.addChild("VisualModel")
floorVisu.loader = floorVisu.addObject('MeshOBJLoader', name="loader", filename="mesh/floor.obj")
floorVisu.addObject('OglModel', name="model", src="@loader", scale3d=[5.0]*3, color=[1., 1., 0.], updateNormals=False)
floorVisu.addObject('RigidMapping')

## Slide 18: SOFA – Using runSofa GUI

## Slide 19: SOFA – Using runSofa GUI
# Collision pipeline
rootNode.addObject('DefaultPipeline')
rootNode.addObject('FreeMotionAnimationLoop')
rootNode.addObject('GenericConstraintSolver', tolerance="1e-6", maxIterations="1000")
rootNode.addObject('BruteForceBroadPhase')
rootNode.addObject('BVHNarrowPhase')
rootNode.addObject('RuleBasedContactManager', responseParams="mu="+str(0.0), name='Response', response='FrictionContactConstraint')
rootNode.addObject('LocalMinDistance', alarmDistance=10, contactDistance=5, angleCone=0.01)
#### Collision subnode for the sphere
collision = sphere.addChild('collision')
collision.addObject('MeshOBJLoader', name="loader", filename="mesh/ball.obj", triangulate="true", scale=45.0)
collision.addObject('MeshTopology', src="@loader")
collision.addObject('MechanicalObject')
collision.addObject('TriangleCollisionModel')
collision.addObject('LineCollisionModel')
collision.addObject('PointCollisionModel')
collision.addObject('RigidMapping')

## Slide 20: SOFA – Using runSofa GUI
#### Collision subnode for the floor
floorCollis = floor.addChild('collision')
floorCollis.addObject('MeshOBJLoader', name="loader", filename="mesh/floor.obj", triangulate="true", scale=5.0)
floorCollis.addObject('MeshTopology', src="@loader")
floorCollis.addObject('MechanicalObject')
floorCollis.addObject('TriangleCollisionModel', moving=False, simulated=False)
floorCollis.addObject('LineCollisionModel', moving=False, simulated=False)
floorCollis.addObject('PointCollisionModel', moving=False, simulated=False)
floorCollis.addObject('RigidMapping')

## Slide 21: SOFA Main Principles
Scene Graph:
  Each object can have several models in SOFA:
    Mechanical model
    Actuation model
    Collision model
    Visual model

## Slide 22: SOFA Main Principles
1. Scene Graph Example:

## Slide 23: SOFA Main Principles
1. Scene Graph Example:

## Slide 24: SOFA Main Principles
Animation loop & Visitors
  Global variables: the time step, gravity field and type of contacts
  Updates the scene, rules and orders for all simulation steps
  The Animation loop:
    It builds and solves the linear systems of differential equations that are present in the simulation
    It solves collisions and constraints
    It updates the scene
  At each time step, the animation loop triggers each event through a Visitor mechanism

## Slide 25: SOFA Main Principles
Several Animation loops:
  DefaultAnimationLoop: solves the constraints and the collision together
  FreeMotionAnimationLoop: uses the “free” solution. Collisions and constraints are added to the outcomes via a correction factor
  Multistep: computes several collisions and integration in one single simulation time step
Visitors traverse the scene top-down and bottom-up and call the corresponding virtual functions at each graph node

## Slide 26: SOFA Main Principles
Mapping
  Matching mechanism: gives the
correspondence between models
  Each object can have several models in SOFA:
    Mechanical model
    Collision model
    Visual model
  Each model can rely on a different representation/topology

## Slide 27: SOFA Simulation Features
Topology:
  Describes the geometry
  Discretization of the space in elements, with their connectivity (Finite element Method)
  In real-time surgery simulation and can be hierarchically decomposed into k-cells
  Mappings links the elements

## Slide 28: SOFA Simulation Features
Collision:
  Geometrical representation supporting collisions
Collision Pipeline:
  Executed in the animation loop
  Broad phase: create boxes around the object and the
intersection between them (no intersection = no collision)
  Narrow phase (Distance maps, Layer depth image):
    occur only if there is an intersection in the previous step
    Computation of intersection (descending hierarchy)
  Response: applying forces depending on what occurs. Penalty method (proportional force), Lagrange multiplier constraint (in FreeMotionAnimationLoop)

## Slide 29: SOFA CORE + Plugins
SOFA Core has built-in features:
  Topology loaders
  Solvers: iterative, direct, etc…
  Physical models: FEM based, Iper-elastic, etc…
  Collision computation
Plugins:
  Developed by research groups
  Most used: SofaPython (3)
    Ease the writing of a scene
    Dynamic modifications

## Slide 30: SOFA Application